## Slide 1
Domestic Energy Use in England
Key Findings from the 2011 Energy Follow‑Up Survey (EFUS)
October 23, 2025

## Slide 2
Key Findings & Implications
Zone 1 (living room) vs Zone 2 (other rooms) temperatures differ by about 0.6°C, far less than the 1.3°C assumed in SAP models.
Weekend and weekday mean temperatures are essentially identical, contrary to model assumptions.
Median annual gas consumption is ~14,000 kWh and electricity ~3,700 kWh; consumption scales with dwelling size and occupancy.
Centrally heated homes run heating ~8–9 hours/day, while non‑centrally heated homes run it up to 15 hours/day.
Temperature Gap
Heating Duration
Energy Use
Behaviour Patterns
[1] [2] [3] [4]

## Slide 3
Heating Season Mean Temperatures
Chart: 
| Living Room | Hallway | Bedroom | Zone 2 | External
Mean Temperature (°C) | 19.3 | 18.8 | 18.9 | 18.8 | 9
Living rooms average ~19.3°C and other rooms ~18.8–18.9°C during the heating season.
External mean temperatures are much lower (~9°C), highlighting the heating demand gap.
Difference between zone 1 and zone 2 temperatures (~0.6°C) is smaller than SAP’s 1.3°C assumption.
[5] [6]

## Slide 4
Heating Hours & Energy Use
 | Centrally heated | Non‑centrally heated
Share of households | 90% | 10%
Median daily heating hours (householder) | 8.4–8.8 hrs | 10.7–15.3 hrs
Median daily heating hours (temperature) | 8.8–9.5 hrs | 9.1–16.5 hrs
Typical heating periods | 2 periods (69%); 1 period (21%) | 1 period (81%); 2+ periods (10%)
Median Consumption Gas: ~14,000 kWh/yr Electricity: ~3,700 kWh/yr
Gas use scales with floor area; electricity scales with occupancy and size.
[7] [8] [9] [10]

## Slide 5
Conclusions & Policy Implications
Calibrate energy models: adopt smaller temperature differential (0.6°C vs 1.3°C) and equalise weekend/weekday patterns.
Use realistic heating periods: shorten heating season to 6–7 months and reflect actual daily hours for different system types.
Target insulation & occupancy: consumption rises with dwelling size and occupant numbers; improved insulation reduces gas use.
Policy focus: support elderly and fuel‑poor households to achieve comfortable temperatures without overspending.
Comfort & Efficiency
[11] [12] [13] [14]